## Slide 1
Indian Institute of Science, Bangalore
Artifact Removal for
ICMS-Evoked LFP Recordings
Ramya Sree Galanki • M. Tech Signal Processing, Department of ECE, IISc
Advisors: Prof. Chandra R. Murthy • Prof. Supratim Ray
Motivation & Problem
Intracortical microstimulation introduces large pulse-locked artifacts into simultaneously recorded LFP signals.
These artifacts can be much larger than the neural response of interest.
Artifact shape varies across trials, pulses, and electrodes, so a single fixed template may not be sufficient.
Goal: suppress stimulation artifact while preserving the underlying LFP structure.
Data & Setup
Dataset: GRF_001 ICMS-LFP recordings from NHP Dona.
Conditions compared: no-stimulation and high-stimulation trials.
LFP recordings were analyzed electrode-wise from segmented trial data.
Final real-data validation used 31 selected V1 electrodes.
Main artifact-analysis window: 0–0.4 s after stimulation onset.
Evaluation used FFT error, harmonic artifact error, pulse-triggered residuals, and balanced score.
Methods Compared
Key Findings
Fixed ERP templates reduce the dominant artifact but can leave structured residuals.
PCA suppresses stimulation harmonics strongly, but may risk over-cleaning time-locked neural activity.
SMARTAFull adapts the artifact estimate using local similarity and optimal shrinkage.
In final real-data validation, SMARTAFull gave the best overall artifact reduction across 31 selected V1 electrodes.
Representative Result: SMARTAFull Cleaning
Final Across-electrode Validation
Takeaways
Trial-to-trial and pulse-to-pulse artifact variability limits fixed-template subtraction.
PCA is effective for harmonic suppression but can be aggressive.
SMARTAFull K=3, hp=100 Hz provides the best real-data trade-off between artifact suppression and signal preservation.
ERP Subtraction: fixed average artifact template baseline.
PCA Template K=10: PCA subspace removal for stimulation artifacts.
SMARTALite: local nearest-neighbor pulse-template subtraction.
SMARTAFull K=3, hp=100 Hz: similarity-based artifact estimation with optimal shrinkage; final selected method.
SMARTAFull workflow: Pulse segments → high-pass similarity features → nearest neighbors → optimal shrinkage → local template subtraction → cleaned LFP
Electrode 7: SMARTAFull reduces stimulation-related harmonic structure and moves the high-stimulation spectrum closer to the no-stimulation reference.
Across 31 selected V1 electrodes, SMARTAFull achieved the lowest mean total FFT error and lowest stimulation-harmonic excess error among the tested methods.
Evaluation Metrics
Total FFT error: spectral distance from no-stimulation reference.
Harmonic excess error: residual stimulation-related harmonic power.
Pulse-triggered residual: remaining pulse-locked artifact after cleaning.
Balanced score: combines artifact suppression and signal-preservation criteria.
Why SMARTA?
Fixed templates cannot capture trial-to-trial and pulse-to-pulse artifact variability.
PCA is powerful but may remove time-locked neural activity.
SMARTAFull selects locally similar artifact segments and forms adaptive templates.
OptShrink/optimal shrinkage suppresses noise in the artifact-segment matrix by shrinking unreliable singular values instead of hard-truncating components.
Final validation showed the best overall artifact reduction across selected electrodes.